## Slide 1: FastGC: Accelerate Garbage Collection via an Efficient Copyback-based Data Migration in SSDs
Sheng Yang
2024/03/xx

## Slide 2
SSDs performs out-of-place update due to erase-before-write property of NAND flash memory
Out-of-Place Update
Block 0
Data A
Free
❶ Write data A in block 0
SSDs (Solid State Drives)
Erase-before-write property means the data must be erased before being written in NAND flash memory.

## Slide 3
SSDs performs out-of-place update due to erase-before-write property of NAND flash memory
Out-of-Place Update
Block 0
Data A
Free
Block 0
Old Data A
Data A
❶ Write data A in block 0
❷ Update data A in block 0 (& mapping table)
SSDs (Solid State Drives)
Erase-before-write property means the data must be erased before being written in NAND flash memory.

## Slide 4
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Invalid data means the old data.

## Slide 5
Block 0 (1)
Old Page A
Page A
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Invalid Page: 1
Invalid data means the old data.
(1) Select a victim block to erase
(2) Move valid pages' data
(3) Update remapping table
(4) Erase that victim block

## Slide 6
Block 0 (1)
Old Page A
Page A
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Invalid data means the old data.
Page A
Move
(2)
Invalid Page: 2
(1) Select a victim block to erase
(2) Move valid pages' data
(3) Update remapping table
(4) Erase that victim block

## Slide 7
Block 0 (1, 4)
Free
Free
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Free Page: 2
Invalid data means the old data.
Move
(2)
Page A
(1) Select a victim block to erase
(2) Move valid pages' data
(3) Update remapping table
(4) Erase that victim block

## Slide 8
Block 0 (1, 4)
Free
Free
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Free Page: 2
Invalid data means the old data.
GC (Garbage Collection)
Move
(2)
Page A
(1) Select a victim block to erase
(2) Move valid pages' data
(3) Update remapping table
(4) Erase that victim block
GC is time-consuming and (2) can take 45% of total GC time

## Slide 9
Utilizing copyback to migrate data for GC performance improvement
Prior Work
NAND flash plane
Page A
Free
Move
Copyback means the internal data move:
(1) TN-29-15: NAND Flash Performance Improvement Using Internal Data Move, https://www.micron.com/-/media/client/global/documents/products/technical-note/nand-flash/tn2915.pdf
(2) KIOXIA 4Gb 1.8V Serial Interface NAND Technical Data Sheet, https://europe.kioxia.com/content/dam/kioxia/newidr/productinfo/datasheet/201910/DST_TC58CYG2S0HRAIJ-TDE_EN_36007.pdf
Copyback characteristics:
Faster than external data move (e.g., 40%)
No error correction

## Slide 10
Utilizing copyback to migrate data for GC performance improvement
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
Prior Work
NAND flash plane
Page A
Free
Move
Copyback means the internal data move:
(1) TN-29-15: NAND Flash Performance Improvement Using Internal Data Move, https://www.micron.com/-/media/client/global/documents/products/technical-note/nand-flash/tn2915.pdf
(2) KIOXIA 4Gb 1.8V Serial Interface NAND Technical Data Sheet, https://europe.kioxia.com/content/dam/kioxia/newidr/productinfo/datasheet/201910/DST_TC58CYG2S0HRAIJ-TDE_EN_36007.pdf
ECC (Error Correction Code)
Copyback characteristics:
Faster than external data move (e.g., 40%)
No error correction
TCBGC data migration:
❶ Read data to detect error externally
❷ Copyback data if no error is detected
❶
❷

## Slide 11
Utilizing copyback to migrate data for GC performance improvement
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
Prior Work
NAND flash plane
Page A
Free
Move
Copyback characteristics:
Faster than external data move (e.g., 40%)
No error correction
TCBGC data migration:
❶ Read data to detect error externally
❷ Copyback data if no error is detected
Otherwise,
❸ Correct error if error is detected,
and program data externally
❶
❷
❸
Copyback means the internal data move:
(1) TN-29-15: NAND Flash Performance Improvement Using Internal Data Move, https://www.micron.com/-/media/client/global/documents/products/technical-note/nand-flash/tn2915.pdf
(2) KIOXIA 4Gb 1.8V Serial Interface NAND Technical Data Sheet, https://europe.kioxia.com/content/dam/kioxia/newidr/productinfo/datasheet/201910/DST_TC58CYG2S0HRAIJ-TDE_EN_36007.pdf
ECC (Error Correction Code)

## Slide 12
Prior works have limited performance improvement for error correction
Problem
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
NAND flash plane
Page A
Free
Move
❶
❷
❸

## Slide 13
Prior works have limited performance improvement for error correction
Problem
Access latency of data migration:
Access latency is still high due to ❶
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
NAND flash plane
Page A
Free
Move
❶
❷
❸

## Slide 14
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle means the program/erase cycle
Copyback count
Raw bit error rate
P/E cycle = 4500
P/E cycle = 3000
P/E cycle = 1500
Notes: X and Y axis

## Slide 15
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
P/E cycle = 1500
Notes: ECC

## Slide 16
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
Two key observations:
P/E cycle = 1500
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes

## Slide 17
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
Two key observations:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
P/E cycle = 1500
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes
Error correction

## Slide 18
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
Two key observations:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
(2) The secure copyback counts gradually decease as P/E cycles increase, ending up at zero
P/E cycle = 1500
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes
Error correction
Secure copyback counts

## Slide 19
Key observation:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
(2) The secure copyback counts gradually decease as P/E cycles increase, ending up at zero
Goal:
An algorithm that dynamically selects secure copyback counts:
Utilizing copyback-based data migration efficiently
Maintaining high reliability
FastGC

## Slide 20
Goal: To efficiently utilize copyback-based data migration in GC to improve system performance
Idea:
An efficient copyback feasibility detector which utilizes the threshold copyback count as an indicator to accelerate copyback feasibility detection.
It utilizes copyback error characteristics to efficiently detect copyback feasibility of data instead of transferring out all valid data for detecting.
FastGC

## Slide 21
Proposal:
(1) An efficient copyback feasibility detector is proposed, which utilizes copyback execution counts of data as a new indicator of copyback feasibility
(2) A fast garbage collection scheme, called FastGC, which utilizes the new copyback-based data migration scheme to accelerate GC.
FastGC adds a copyback feasibility detector module in the SSD controller to efficiently distinguish whether data can be migrated by copyback or not with a slight overhead. Friendly data organization is applied in FastGC, which is helpful to detect copyback feasibility.
Advantages:
(1) This scheme greatly reduces performance penalty for copyback feasibility detection and accelerates garbage collection.
(2) The overhead is much smaller than transfer latency and decoding latency caused by detecting bit errors since the number of data migration is large.
Overheads:
Proposal

## Slide 22
Result:
Read and write response time are improved by up to 66.3% and 44.2%, respectively.
The copyback errors are resulted by the program interference, read disturb and P/E cycles (Retention error?)
FastGC