## Slide 1: FastGC: Accelerate Garbage Collection via an Efficient Copyback-based Data Migration in SSDs
Sheng Yang
2024/03/xx
Notes: [Welcome] Hello, everyone. My name is Sheng Yang. Today my presentation title is, FastGC: Accelerate Garbage Collection via an Efficient Copyback-based Data Migration in SSDs (slowly + 2s).

## Slide 2
SSDs performs out-of-place update due to erase-before-write property of NAND flash memory
Out-of-Place Update
Block 0
Data A
Free
❶ Write data A in block 0
SSDs (Solid State Drives)
Erase-before-write property means the data must be erased before being written in NAND flash memory.
Notes: [Out-of-Place Update] Firstly, Please let me introduce the concept of out-of-place update in SSDs. NAND flash memory in SSDs has the erase-before-write property, meaning data must be erased before it can be written. Thus, to improve performance, SSDs perform out-of-place update. As shown here, data A, marked in green, is first placed in block 0. To update data A, SSDs write the newest data into a free place, which is already erased instead of the original place, and then update the mapping table to track data A. Note that the old data A becomes invalid, marked in grey.

## Slide 3
SSDs performs out-of-place update due to erase-before-write property of NAND flash memory
Out-of-Place Update
Block 0
Data A
Free
Block 0
Old Data A
Data A
❶ Write data A in block 0
❷ Update data A in block 0 (& mapping table)
SSDs (Solid State Drives)
Erase-before-write property means the data must be erased before being written in NAND flash memory.
Notes: [Out-of-Place Update] Firstly, Please let me introduce the concept of out-of-place update in SSDs. NAND flash memory in SSDs has the erase-before-write property, meaning data must be erased before it can be written. Thus, to improve performance, SSDs perform out-of-place update. As shown here, data A, marked in green, is first placed in block 0. To update data A, SSDs write the newest data into a free place, which is already erased instead of the original place, and then update the mapping table to track data A. Note that the old data A, marked in grey, becomes invalid.

## Slide 4
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Invalid data means the old data.
Notes: [Garbage Collection] Therefore, modern SSDs perform garbage collection, which reclaims free data by erasing invalid data. However, NAND flash memory has asymmetry in operation units, meaning the size of the erase operation is larger than that of the read and write operation. Due to this limitation, garbage collection migrates valid data before erasing the block. For example, we select block 0 as the victim block, which contains 1 invalid page and one valid page. Next, the valid page is migrated from block 0 to another free block. Then, update the mapping table and erase the victim block. Note that now we have two valid pages in block 0. However, GC is time-consuming, and data migration can take 45% of total GC time.

## Slide 5
Block 0 ❶
Old Page A
Page A
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Invalid Page: 1
Invalid data means the old data.
❶ Select a victim block to erase
❷ Move valid pages' data
❸ Update mapping table
❹ Erase that victim block
Notes: [Garbage Collection] Therefore, modern SSDs perform garbage collection, which reclaims free data by erasing invalid data. However, NAND flash memory has asymmetry in operation units, meaning the size of the erase operation is larger than that of the read and write operation. Due to this limitation, garbage collection migrates valid data before erasing the block. For example, we select block 0 as the victim block, which contains 1 invalid page and one valid page. Next, the valid page is migrated from block 0 to another free block. Then, update the mapping table and erase the victim block. Note that now we have two valid pages in block 0. However, GC is time-consuming, and data migration can take 45% of total GC time.

## Slide 6
Block 0 ❶
Old Page A
Page A
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Invalid data means the old data.
Page A
Move
❷
Invalid Page: 2
❶ Select a victim block to erase
❷ Move valid pages' data
❸ Update mapping table
❹ Erase that victim block
Notes: [Garbage Collection] Therefore, modern SSDs perform garbage collection, which reclaims free data by erasing invalid data. However, NAND flash memory has asymmetry in operation units, meaning the size of the erase operation is larger than that of the read and write operation. Due to this limitation, garbage collection migrates valid data before erasing the block. For example, we select block 0 as the victim block, which contains 1 invalid page and one valid page. Next, the valid page is migrated from block 0 to another free block. Then, update the mapping table and erase the victim block. Note that now we have two valid pages in block 0. However, GC is time-consuming, and data migration can take 45% of total GC time.

## Slide 7
Block 0 ❶❹
Free
Free
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Free Page: 2
Invalid data means the old data.
Move
❷
Page A
❶ Select a victim block to erase
❷ Move valid pages' data
❸ Update mapping table
❹ Erase that victim block
Notes: [Garbage Collection] Therefore, modern SSDs perform garbage collection, which reclaims free data by erasing invalid data. However, NAND flash memory has asymmetry in operation units, meaning the size of the erase operation is larger than that of the read and write operation. Due to this limitation, garbage collection migrates valid data before erasing the block. For example, we select block 0 as the victim block, which contains 1 invalid page and one valid page. Next, the valid page is migrated from block 0 to another free block. Then, update the mapping table and erase the victim block. Note that now we have two valid pages in block 0. However, GC is time-consuming, and data migration can take 45% of total GC time.

## Slide 8
Block 0 ❶❹
Free
Free
Reclaims free data by erasing invalid data
Due to asymmetry in operation units of NAND flash memory: (Page) < (Block)
Garbage Collection
Free Page: 2
Invalid data means the old data.
GC (Garbage Collection)
Move
❷
Page A
❶ Select a victim block to erase
❷ Move valid pages' data
❸ Update mapping table
❹ Erase that victim block
GC is time-consuming and ❷ can take 45% of total GC time
Notes: [Garbage Collection] Therefore, modern SSDs perform garbage collection, which reclaims free data by erasing invalid data. However, NAND flash memory has asymmetry in operation units, meaning the size of the erase operation is larger than that of the read and write operation. Due to this limitation, garbage collection migrates valid data before erasing the block. For example, we select block 0 as the victim block, which contains 1 invalid page and one valid page. Next, the valid page is migrated from block 0 to another free block. Then, update the mapping table and erase the victim block. Note that now we have two valid pages in block 0. However, GC is time-consuming, and data migration can take 45% of total GC time.

## Slide 9
Utilizing copyback to migrate data for GC performance improvement
Prior Work
NAND flash plane
Page A
Free
Internal data move
Copyback means the internal data move:
(1) TN-29-15: NAND Flash Performance Improvement Using Internal Data Move, https://www.micron.com/-/media/client/global/documents/products/technical-note/nand-flash/tn2915.pdf
(2) KIOXIA 4Gb 1.8V Serial Interface NAND Technical Data Sheet, https://europe.kioxia.com/content/dam/kioxia/newidr/productinfo/datasheet/201910/DST_TC58CYG2S0HRAIJ-TDE_EN_36007.pdf
Copyback characteristics:
Faster than external data move (e.g., 40%)
No error correction
Notes: [Prior Work] Prior work utilizes copyback to migrate data for GC performance improvement. The copyback is the internal data movement inside a NAND flash plane, faster than external data movement between the NAND chip and SSD controller. Nevertheless, the data movement of copyback is inside the NAND flash plane so that no error correction can be conducted. As a result, prior work called traditional copyback-based GC, migrates data in two ways. First, valid data is read to detect errors externally; if no error is detected, the copyback is conducted for data migration. Otherwise, if the error is detected, the SSD controller will correct the error and then program the data externally.

## Slide 10
Utilizing copyback to migrate data for GC performance improvement
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
Prior Work
NAND flash plane
Page A
Free
Internal data move
Copyback means the internal data move:
(1) TN-29-15: NAND Flash Performance Improvement Using Internal Data Move, https://www.micron.com/-/media/client/global/documents/products/technical-note/nand-flash/tn2915.pdf
(2) KIOXIA 4Gb 1.8V Serial Interface NAND Technical Data Sheet, https://europe.kioxia.com/content/dam/kioxia/newidr/productinfo/datasheet/201910/DST_TC58CYG2S0HRAIJ-TDE_EN_36007.pdf
ECC (Error Correction Code)
Copyback characteristics:
Faster than external data move (e.g., 40%)
No error correction
TCBGC data migration:
❶ Read data to detect error externally
❷ Copyback data if no error is detected
❶
❷
Notes: [Prior Work] Prior work utilizes copyback to migrate data for GC performance improvement. The copyback is the internal data movement inside a NAND flash plane, faster than external data movement between the NAND chip and SSD controller. Nevertheless, the data movement of copyback is inside the NAND flash plane so that no error correction can be conducted. As a result, prior work called traditional copyback-based GC, migrates data in two ways. First, valid data is read to detect errors externally; if no error is detected, the copyback is conducted for data migration. Otherwise, if the error is detected, the SSD controller will correct the error and then program the data externally.

## Slide 11
Utilizing copyback to migrate data for GC performance improvement
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
Prior Work
NAND flash plane
Page A
Free
Internal data move
Copyback characteristics:
Faster than external data move (e.g., 40%)
No error correction
TCBGC data migration:
❶ Read data to detect error externally
❷ Copyback data if no error is detected
Otherwise,
❸ Correct error if error is detected,
and program data externally
(External data move)
❶
❷
❸
Copyback means the internal data move:
(1) TN-29-15: NAND Flash Performance Improvement Using Internal Data Move, https://www.micron.com/-/media/client/global/documents/products/technical-note/nand-flash/tn2915.pdf
(2) KIOXIA 4Gb 1.8V Serial Interface NAND Technical Data Sheet, https://europe.kioxia.com/content/dam/kioxia/newidr/productinfo/datasheet/201910/DST_TC58CYG2S0HRAIJ-TDE_EN_36007.pdf
ECC (Error Correction Code)
Notes: [Prior Work] Prior work utilizes copyback to migrate data for GC performance improvement. The copyback is the internal data movement inside a NAND flash plane, faster than external data movement between the NAND chip and SSD controller. Nevertheless, the data movement of copyback is inside the NAND flash plane so that no error correction can be conducted. As a result, prior work called traditional copyback-based GC, migrates data in two ways. First, valid data is read to detect errors externally; if no error is detected, the copyback is conducted for data migration. Otherwise, if the error is detected, the SSD controller will correct the error and then program the data externally.

## Slide 12
Prior works have limited performance improvement for error correction
Problem
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
NAND flash plane
Page A
Free
Internal data move
❶
❷
❸
Notes: [Problem] Prior works have limited performance improvement for error correction. On the right side, we can see the access latencies of those two data migration methods. Whether an error is detected or not, external data movement is needed for both methods. Therefore, access latency is still high, limiting performance improvement.

## Slide 13
Prior works have limited performance improvement for error correction
Problem
Access latency of data migration:
Access latency is still high due to ❶
SSD controller
Error correction (or ECC)
Traditional copyback-based GC (TCBGC)
NAND flash plane
Page A
Free
Internal data move
❶
❷
❸
Notes: [Problem] Prior works have limited performance improvement for error correction. On the right side, we can see the access latencies of those two data migration methods. Whether an error is detected or not, external data movement is needed for both methods. Therefore, access latency is still high, limiting performance improvement.

## Slide 14
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle means the program/erase cycle
Copyback count
Raw bit error rate
P/E cycle = 4500
P/E cycle = 3000
P/E cycle = 1500
Notes: [Copyback Error Characteristics] To understand copyback error characteristics, this work measured error rate by moving data between blocks with same P/E cycle via copyback. Here is the chart of copyback error distribution, where the copyback count is on the x-axis, and the raw bit error rate is on the y-axis.

## Slide 15
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
P/E cycle = 1500
Notes: [Copyback Error Characteristics] To understand copyback error characteristics, this work measured error rate by moving data between blocks with same P/E cycle via copyback. Here is the chart of copyback error distribution, where the copyback count is on the x-axis, and the raw bit error rate is on the y-axis. And the red horizontal line illustrates the error correction capability of ECC.

## Slide 16
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
Two key observations:
P/E cycle = 1500
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes
Notes: [Copyback Error Characteristics] To understand copyback error characteristics, this work measured error rate by moving data between blocks with same P/E cycle via copyback. Here is the chart of copyback error distribution, where the copyback count is on the x-axis, and the raw bit error rate is on the y-axis. And the red horizontal line illustrates the error correction capability of ECC. By marking the intersection between the error rate curves and the red horizontal line, we have two key observations.

## Slide 17
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
Two key observations:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
P/E cycle = 1500
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes
Error correction
Notes: [Copyback Error Characteristics] To understand copyback error characteristics, this work measured error rate by moving data between blocks with same P/E cycle via copyback. Here is the chart of copyback error distribution, where the copyback count is on the x-axis, and the raw bit error rate is on the y-axis. And the red horizontal line illustrates the error correction capability of ECC. By marking the intersection between the error rate curves and the red horizontal line, we have two key observations. The first one is that ECC can protect against data loss within a certain number of copyback operations under different P/E cycles, as the green rectangle shows.

## Slide 18
Copyback count
Raw bit error rate
Move data between blocks with same P/E cycle via copyback to measure error rate
Copyback Error Characteristics
P/E cycle = 4500
P/E cycle = 3000
Error correction capability of ECC
Two key observations:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
(2) The secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero
P/E cycle = 1500
P/E cycle means the program/erase cycle
This ECC can protect data under the raw bit error rate of (120 / (1024 * 8)) = 0.0146484375, with 120 bits correction per 1024 bytes
Error correction
Secure threshold copyback counts
Notes: [Copyback Error Characteristics] To understand copyback error characteristics, this work measured the error rate by moving data between blocks with the same P/E cycle via copyback. Here is the chart of copyback error distribution, where the copyback count is on the x-axis, and the raw bit error rate is on the y-axis. The red horizontal line illustrates ECC's error correction capability. We have two key observations by marking the intersection between the error rate curves and the red horizontal line. The first one is that ECC can protect against data loss within a certain number of copyback operations under different P/E cycles, as the green rectangle shows. The second one is that the secure threshold copyback counts, where the error rate is under the error correction capability of ECC, gradually decrease as P/E cycles increase, ending up at zero.

## Slide 19
Key observation:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
(2) The secure threshold copyback counts gradually decease as P/E cycles increase, ending up at zero
FastGC
Notes: [FastGC] Therefore, here comes to their work. Based on those two key observations, the goal of their paper is to develop an algorithm that decides whether data can be migrated by copyback with correctable error to utilize copyback-based data migration efficiently and maintain high reliability. The below Figure shows the victim and free block organization in their proposal. User data is managed at the page granularity. Two free blocks are selected to store valid data for each victim block to erase. One free block is from the same NAND flash plane as the victim block. Another one is from the global block set, which could come from other NAND chips.

## Slide 20
Key observation:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
(2) The secure threshold copyback counts gradually decease as P/E cycles increase, ending up at zero
Goal:
An algorithm that decides whether data can be migrated by copyback with correctable error:
Utilizing copyback-based data migration efficiently
Maintaining high reliability
FastGC
Notes: [FastGC] Therefore, here comes to their work. Based on those two key observations, the goal of their paper is to develop an algorithm that decides whether data can be migrated by copyback with correctable error to utilize copyback-based data migration efficiently and maintain high reliability. The below Figure shows the victim and free block organization in their proposal. User data is managed at the page granularity. Two free blocks are selected to store valid data for each victim block to erase. One free block is from the same NAND flash plane as the victim block. Another one is from the global block set, which could come from other NAND chips.

## Slide 21
Key observation:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
(2) The secure threshold copyback counts gradually decease as P/E cycles increase, ending up at zero
Goal:
An algorithm that decides whether data can be migrated by copyback with correctable error:
Utilizing copyback-based data migration efficiently
Maintaining high reliability
FastGC
Victim and free block organization
Victim Block 0
Page A
Free Block 0
Free Block 1
Notes: [FastGC] Therefore, here comes to their work. Based on those two key observations, the goal of their paper is to develop an algorithm that decides whether data can be migrated by copyback with correctable error to utilize copyback-based data migration efficiently and maintain high reliability. The below Figure shows the victim and free block organization in their proposal. User data is managed at the page granularity. Two free blocks are selected to store valid data for each victim block to erase. One free block is from the same NAND flash plane as the victim block. Another one is from the global block set, which could come from other NAND chips.

## Slide 22
Key observation:
(1) ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
(2) The secure threshold copyback counts gradually decease as P/E cycles increase, ending up at zero
Goal:
An algorithm that decides whether data can be migrated by copyback with correctable error:
Utilizing copyback-based data migration efficiently
Maintaining high reliability
FastGC
Victim and free block organization
NAND flash plane
Victim Block 0
Page A
Free Block 0
Global Block Set
Free Block 1
Notes: [FastGC] Therefore, here comes to their work. Based on those two key observations, the goal of their paper is to develop an algorithm that decides whether data can be migrated by copyback with correctable error to utilize copyback-based data migration efficiently and maintain high reliability. The below Figure shows the victim and free block organization in their proposal. User data is managed at the page granularity. Two free blocks are selected to store valid data for each victim block to erase. One free block is from the same NAND flash plane as the victim block. Another one is from the global block set, which could come from other NAND chips.

## Slide 23
Copyback Feasibility Detector
?
Page A
Free Block 0
Copyback
Free Block 1
External data move
Notes: [Copyback Feasibility Detector] To utilize copyback-based data migration efficiently, their algorithm detects the copyback feasibility by comparing the copyback count of a valid page and the secure threshold copyback count of the free block in the same plane. In example 1, the copyback count 0 is smaller than the secure threshold copyback 5. Thus, data is migrated by copyback, and the copyback count is incremented by 1. In example 1, the copyback count 6 is larger than the secure threshold copyback. Hence, data is migrated by external data movement, and the copyback count is reset to zero. To achieve this detection, they designed a copyback feasibility detector in the SSD controller.

## Slide 24
Copyback Feasibility Detector
?
The secure threshold copyback count of block with 1500 P/E cycles is 5
Page A
Free Block 0
Copyback
Free Block 1
External data move
Example 1:
(1)
(2)
(3) Migrate data by copyback
(4)
Notes: [Copyback Feasibility Detector] To utilize copyback-based data migration efficiently, their algorithm detects the copyback feasibility by comparing the copyback count of a valid page and the secure threshold copyback count of the free block in the same plane. In example 1, the copyback count 0 is smaller than the secure threshold copyback 5. Thus, data is migrated by copyback, and the copyback count is incremented by 1. In example 1, the copyback count 6 is larger than the secure threshold copyback. Hence, data is migrated by external data movement, and the copyback count is reset to zero. To achieve this detection, they designed a copyback feasibility detector in the SSD controller.

## Slide 25
Copyback Feasibility Detector
?
The secure threshold copyback count of block with 1500 P/E cycles is 5
Page A
Free Block 0
Copyback
Free Block 1
External data move
Example 2:
(1)
(2)
(3) Migrate data by external data move
(4)
Example 1:
(1)
(2)
(3) Migrate data by copyback
(4)
Notes: [Copyback Feasibility Detector] To utilize copyback-based data migration efficiently, their algorithm detects the copyback feasibility by comparing the copyback count of a valid page and the secure threshold copyback count of the free block in the same plane. In example 1, the copyback count 0 is smaller than the secure threshold copyback 5. Thus, data is migrated by copyback, and the copyback count is incremented by 1. In example 1, the copyback count 6 is larger than the secure threshold copyback. Hence, data is migrated by external data movement, and the copyback count is reset to zero. To achieve this detection, they designed a copyback feasibility detector in the SSD controller.

## Slide 26
Copyback Feasibility Detector
?
The secure threshold copyback count of block with 1500 P/E cycles is 5
A hardware called copyback feasibility detector in SSD controller compares the counts
Page A
Free Block 0
Copyback
Free Block 1
External data move
Example 1:
(1)
(2)
(3) Migrate data by copyback
(4)
Example 2:
(1)
(2)
(3) Migrate data by external data move
(4)
Notes: [Copyback Feasibility Detector] To utilize copyback-based data migration efficiently, their algorithm detects the copyback feasibility by comparing the copyback count of a valid page and the secure threshold copyback count of the free block in the same plane. In example 1, the copyback count 0 is smaller than the secure threshold copyback 5. Thus, data is migrated by copyback, and the copyback count is incremented by 1. In example 1, the copyback count 6 is larger than the secure threshold copyback. Hence, data is migrated by external data movement, and the copyback count is reset to zero. To achieve this detection, they designed a copyback feasibility detector in the SSD controller.

## Slide 27
Copyback Error Aware Data Migration
NAND flash plane
Page A
Free Block 0
Copyback
Global Block Set
Free Block 1
❶
Access latency of data migration:
Notes: [Copyback Error Aware Data Migration] Next, based on the result of the copyback feasibility detector, let us see the access latencies of data migration. If copyback is conducted, no valid data is read into the SSD controller for error correction. On the other hand, if external data movement is conducted, valid data is read into the SSD controller for error correction and then programmed into the global block set. Note that access latency for reading copyback count is needed in both methods, where that data is stored in NAND memory. After adding that access latency, both methods’ latencies are increased. However, the best case, which uses the copyback, is still faster than the prior work since the metadata size is smaller than the page size.

## Slide 28
Copyback Error Aware Data Migration
NAND flash plane
Page A
Free Block 0
Copyback
Global Block Set
Free Block 1
SSD controller
Error correction (or ECC)
❶
❷
❸
Access latency of data migration:
Notes: [Copyback Error Aware Data Migration] Next, based on the result of the copyback feasibility detector, let us see the access latencies of data migration. If copyback is conducted, no valid data is read into the SSD controller for error correction. On the other hand, if external data movement is conducted, valid data is read into the SSD controller for error correction and then programmed into the global block set. Note that access latency for reading copyback count is needed in both methods, where that data is stored in NAND memory. After adding that access latency, both methods’ latencies are increased. However, the best case, which uses the copyback, is still faster than the prior work since the metadata size is smaller than the page size.

## Slide 29
Copyback Error Aware Data Migration
NAND flash plane
Page A
Free Block 0
Copyback
Global Block Set
Free Block 1
SSD controller
Error correction (or ECC)
❶
❷
❸
Access latency of data migration:
Access latency for reading copyback count is needed
Copyback feasibility detector
Notes: [Copyback Error Aware Data Migration] Next, based on the result of the copyback feasibility detector, let us see the access latencies of data migration. If copyback is conducted, no valid data is read into the SSD controller for error correction. On the other hand, if external data movement is conducted, valid data is read into the SSD controller for error correction and then programmed into the global block set. Note that access latency for reading copyback count is needed in both methods, where that data is stored in NAND memory. After adding that access latency, both methods’ latencies are increased. However, the best case, which uses the copyback, is still faster than the prior work since the metadata size is smaller than the page size.

## Slide 30
Copyback Error Aware Data Migration
NAND flash plane
Page A
Free Block 0
Copyback
Global Block Set
Free Block 1
SSD controller
Error correction (or ECC)
❶
❷
❸
Access latency of data migration:
Access latency for reading copyback count is needed:
Copyback feasibility detector
❹
Notes: [Copyback Error Aware Data Migration] Next, based on the result of the copyback feasibility detector, let us see the access latencies of data migration. If copyback is conducted, no valid data is read into the SSD controller for error correction. On the other hand, if external data movement is conducted, valid data is read into the SSD controller for error correction and then programmed into the global block set. Note that access latency for reading copyback count is needed in both methods, where that data is stored in NAND memory. After adding that access latency, both methods’ latencies are increased. However, the best case, which uses the copyback, is still faster than the prior work since the metadata size is smaller than the page size.

## Slide 31
Summary
Background & Problem:
1. GC is time-consuming and data migration time can take 45% of total GC time
2. Prior works have limited performance improvement for error correction
Notes: [Summary] In conclusion. First, I described their research background, that GC is time-consuming and data migration time can take 45% of total GC time. The common problem in prior work is that prior work has limited performance improvement for error correction. Then, we observed that ECC can protect against data loss within a certain number of copyback operations under different P/E cycles, and the secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero. Therefore, the goal of their work is to design an algorithm that decides whether data can be migrated by copyback with correctable error so that they can utilize copyback-based data migration efficiently and maintain high reliability. To achieve their goal, the idea is to utilize the secure threshold copyback count as an indicator to accelerate data migration. The overhead in their work is a 1-byte copyback count for each page and metadata transfer latency for detecting copyback feasibility.
Thank you very much!

## Slide 32
Summary
Background & Problem:
1. GC is time-consuming and data migration time can take 45% of total GC time
2. Prior works have limited performance improvement for error correction
Key observations:
1. ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
2. The secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero
Notes: [Summary] In conclusion. First, I described their research background, that GC is time-consuming and data migration time can take 45% of total GC time. The common problem in prior work is that prior work has limited performance improvement for error correction. Then, we observed that ECC can protect against data loss within a certain number of copyback operations under different P/E cycles, and the secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero. Therefore, the goal of their work is to design an algorithm that decides whether data can be migrated by copyback with correctable error so that they can utilize copyback-based data migration efficiently and maintain high reliability. To achieve their goal, the idea is to utilize the secure threshold copyback count as an indicator to accelerate data migration. The overhead in their work is a 1-byte copyback count for each page and metadata transfer latency for detecting copyback feasibility.
Thank you very much!

## Slide 33
Summary
Background & Problem:
1. GC is time-consuming and data migration time can take 45% of total GC time
2. Prior works have limited performance improvement for error correction
Key observations:
1. ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
2. The secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero
Goal:
An algorithm that decides whether data can be migrated by copyback with correctable error:
Utilizing copyback-based data migration efficiently
Maintaining high reliability
Notes: [Summary] In conclusion. First, I described their research background, that GC is time-consuming and data migration time can take 45% of total GC time. The common problem in prior work is that prior work has limited performance improvement for error correction. Then, we observed that ECC can protect against data loss within a certain number of copyback operations under different P/E cycles, and the secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero. Therefore, the goal of their work is to design an algorithm that decides whether data can be migrated by copyback with correctable error so that they can utilize copyback-based data migration efficiently and maintain high reliability. To achieve their goal, the idea is to utilize the secure threshold copyback count as an indicator to accelerate data migration. The overhead in their work is a 1-byte copyback count for each page and metadata transfer latency for detecting copyback feasibility.
Thank you very much!

## Slide 34
Summary
Background & Problem:
1. GC is time-consuming and data migration time can take 45% of total GC time
2. Prior works have limited performance improvement for error correction
Key observations:
1. ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
2. The secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero
Goal:
An algorithm that decides whether data can be migrated by copyback with correctable error:
Utilizing copyback-based data migration efficiently
Maintaining high reliability
Idea:
Utilizing the secure threshold copyback count as an indicator to accelerate data migration.
Notes: [Summary] In conclusion. First, I described their research background, that GC is time-consuming and data migration time can take 45% of total GC time. The common problem in prior work is that prior work has limited performance improvement for error correction. Then, we observed that ECC can protect against data loss within a certain number of copyback operations under different P/E cycles, and the secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero. Therefore, the goal of their work is to design an algorithm that decides whether data can be migrated by copyback with correctable error so that they can utilize copyback-based data migration efficiently and maintain high reliability. To achieve their goal, the idea is to utilize the secure threshold copyback count as an indicator to accelerate data migration. The overhead in their work is a 1-byte copyback count for each page and metadata transfer latency for detecting copyback feasibility.
Thank you very much!

## Slide 35
Summary
Background & Problem:
1. GC is time-consuming and data migration time can take 45% of total GC time
2. Prior works have limited performance improvement for error correction
Key observations:
1. ECC can protect against data loss within a certain number of copyback operations under different P/E cycles
2. The secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero
Goal:
An algorithm that decides whether data can be migrated by copyback with correctable error:
Utilizing copyback-based data migration efficiently
Maintaining high reliability
Idea:
Utilizing the secure threshold copyback count as an indicator to accelerate data migration.
Overheads:
1-byte copyback count for each page
Metadata transfer latency for detecting copyback feasibility (< transfer latency of 1 page in TCBGC)
Notes: [Summary] In conclusion. First, I described their research background, that GC is time-consuming and data migration time can take 45% of total GC time. The common problem in prior work is that prior work has limited performance improvement for error correction. Then, we observed that ECC can protect against data loss within a certain number of copyback operations under different P/E cycles, and the secure threshold copyback counts gradually decrease as P/E cycles increase, ending up at zero. Therefore, the goal of their work is to design an algorithm that decides whether data can be migrated by copyback with correctable error so that they can utilize copyback-based data migration efficiently and maintain high reliability. To achieve their goal, the idea is to utilize the secure threshold copyback count as an indicator to accelerate data migration. The overhead in their work is a 1-byte copyback count for each page and metadata transfer latency for detecting copyback feasibility.
Thank you very much!

## Slide 36
Proposal:
(1) An efficient copyback feasibility detector is proposed, which utilizes copyback execution counts of data as a new indicator of copyback feasibility
(2) A fast garbage collection scheme, called FastGC, which utilizes the new copyback-based data migration scheme to accelerate GC.
FastGC adds a copyback feasibility detector module in the SSD controller to efficiently distinguish whether data can be migrated by copyback or not with a slight overhead. Friendly data organization is applied in FastGC, which is helpful to detect copyback feasibility.
Advantages:
(1) This scheme greatly reduces performance penalty for copyback feasibility detection and accelerates garbage collection.
(2) The overhead is much smaller than transfer latency and decoding latency caused by detecting bit errors since the number of data migration is large.
Overheads:
Proposal

## Slide 37
Result:
Read and write response time are improved by up to 66.3% and 44.2%, respectively.
The copyback errors are resulted by the program interference, read disturb and P/E cycles (Retention error?)
FastGC